## Slide 1: Lab 3 IPC Scalability
ex13_notifypeer

## Slide 2: Overview
This is an example of scaling IPC down to just Notify.
Goals
  Add an EVE processor to an existing two processor application.
  IPC scalability, Notify only
  Use a SYS/BIOS Event object to wait on two input sources

## Slide 3: ex13_notifypeer
Initial setup is for two processors; HOST and DSP1
HOST uses message queue to send jobs to DSP1.
You will modify DSP1 to forward the job to EVE1.
You will add EVE1 to application using only IPC Notify.

## Slide 4: Initial Data Flow
Heap
HOST
msg
DSP1
Client
serverQ: MessageQ
Message
Pool
1
2
3
SharedRegion
NULL: MessageQ
Server
msg
msg
msg
4
5
6

## Slide 5: Final Data Flow
HOST
msg
DSP1
Client
serverQ: MessageQ
NULL: MessageQ
Server
msg
msg
EVE1
Process
NotifyCB
: Semaphore
: Semaphore
NotifyCB
2
3
4
5
6
7
8
9
10
11
12
13
msg
1

## Slide 6: Step 1 — Work Area
Create a work folder for this lab
  C:\TI_Demo
Extract the example into the work folder
  <ipc_3_30_pp_bb>\examples\DRA7XX_bios_elf\ex13_notifypeer.zip

## Slide 7: Step 2 — Build Environment
Set the product install paths as defined by your physical environment.
  Edit ex13_notifypeer/products.mak
  DEPOT = C:/Products IPC_INSTALL_DIR = $(DEPOT)/ipc_m_mm_pp_bb BIOS_INSTALL_DIR = $(DEPOT)/bios_m_mm_pp_bb XDC_INSTALL_DIR = $(DEPOT)/xdctools_m_mm_pp_bb
Set the tool paths (only need the ones you actually plan to use).
  Edit ex13_notifypeer/products.mak
  CCS = C:/CCS/CCS_6_0_0_00190/ccsv6/tools/compiler gnu.targets.arm.A15F = $(CCS)/gcc_arm_none_eabi_m_m_p ti.targets.elf.C66 = $(CCS)/c6000_m_m_p ti.targets.arm.elf.M4 = $(CCS)/arm_m_m_p ti.targets.arp32.elf.ARP32_far = $(CCS)/arp32_m_m_p
Each example has its own products.mak file; you may also create a products.mak file in the parent directory which will be used by all examples.

## Slide 8: Step 3 — Build Executables
Open a Windows Command Prompt
  Start > Run cmd
TIP: Use the following command to create an alias for the make command
  doskey make="C:\Products\xdctools_3_30_04_52\gmake.exe" $*
TIP: Use dosrc.bat to setup your build environment
  <ipc_3_30_pp_bb>/examples/dosrc.bat — copy to your work folder
  Edit dosrc.bat, set product paths
  Run script in your command prompt
Build the example
  cd ex13_notifypeer make
The executables will be in their respective "bin" folders
  ex13_notifypeer\host\bin\debug\app_host.xa15fg ex13_notifypeer\dsp1\bin\debug\server_dsp1.xe66

## Slide 9: CCS Auto Run Configuration
Disable Run to Main in your target configuration.
  Target Configurations
  Projects > TargetConfiguration > DRA7xx_EVM.ccxml
  RMB > Properties
  Device (menu) > C66xx_DSP1
  Auto Run and Launch Options > Select
  Auto Run Options (group) > On a program load or restart > Unselect
  Use the Device pull-down menu to select the next processor. Repeat for each processor.
Notes: Does this slide need a screen shot?

## Slide 10: Step 4 — Load Processors
Load HOST with executable
  Debug view > CortexA15_0 > Select
  Run > Load > Load Program
  Click Browse, select the HOST executable
  ex13_notifypeer\host\bin\debug\app_host.xa15fg
Load DSP1 with executable
  Debug view > C66xx_DSP1 > Select
  Run > Load > Load Program
  Click Browse, select the DSP1 executable
    ex13_notifypeer\dsp1\bin\debug\server_dsp1.xe66

## Slide 11: Step 5 — Run the Example
Run HOST processor
  Debug view > CortexA15_0 > Select
  Run > Resume
Run DSP1 processor
  Debug view > C66xx_DSP1 > Select
  Run > Resume
The example completes very quickly
Halt DSP1 processor
  Debug view > C66xx_DSP1 > Select
  Run > Suspend
Halt HOST processor
  Debug view > CortexA15_0 > Select
  Run > Suspend

## Slide 12: ROV — LoggerBuf Module
When the example completes, use ROV to inspect the LoggerBuf module to see the log events.
  Debug view > CortexA15_0 > Select
  RTOS Object View (ROV) > LoggerBuf > Select
  Records (tab) > Select
  AppLog > Select (don’t open it)
You will see a list of log events.

## Slide 13: Step 6 — Adding EVE1 Processor
To build the EVE1 executable, you need to edit the top-level makefile. Add EVE1 to the PROCLIST macro.
  Edit ex13_notifypeer/makefile
  PROCLIST = dsp1 eve1 host
To enable DSP1 to EVE1 IPC communication, edit the server source file and uncomment the EVE macro.
  Edit ex13_notifypeer/dsp1/Server.c
  /* define the EVE peer */ #define EVE "EVE1"
Build the example
  cd ex13_notifypeer make

## Slide 14: Step 7 — Connect to EVE1 Processor
Load GEL file. Needed for programming the MMU.
  CS_DAP_DebugSS > Select (must show all cores to see the DebugSS)
  Tools > GEL Files
  GEL Files (view) > GEL Files Panel (right side) > RMB > Load GEL...
  ex13_notifypeer/eve1/ex13_notifypeer_eve1.gel
Connect to EVE1
  CortexA15_0 > Select
  Scripts > DRA7xx MULTICORE Initialization > EVE1SSClkEnable_API
  CS_DAP_DebugSS > Select
  Scripts > EVE MMU Configuration > ex13_notifypeer_eve1_mmu_config
  ARP32_EVE_1 > RMB > Connect Target
  Run > Reset > CPU Reset
Notes: Note: With EVE, you program MMU before connecting, unlike with the IPU.

## Slide 15: Step 8 — Load Processors
Reload HOST with executable
  Reset HOST
  Run > Load > Reload Program
Reload DSP1 with executable
  Reset DSP1
  Run > Load > Reload Program
Load EVE1 with executable
  Debug view > ARP32_EVE_1 > Select
  Run > Load > Load Program
  Click Browse, select the EVE1 executable
    ex13_notifypeer\eve1\bin\debug\alg_eve1.xearp32F

## Slide 16: Step 9 — Run the Example
Run HOST processor
  Debug view > CortexA15_0 > Select
  Run > Resume
Run EVE1 processor
  Debug view > ARP32_EVE_1 > Select
  Run > Resume
Run DSP1 processor
  Debug view > C66xx_DSP1 > Select
  Run > Resume
The example completes quickly. Halt all three processors.

## Slide 17: Inspect the Logs
Use ROV to inspect the logs from each processor.
The HOST logs should look identical.

## Slide 18: Inspect the Logs
The DSP1 logs will contain additional EVE notifications.

## Slide 19: Inspect the Logs
The EVE logs contain the jobs messages.

## Slide 20: IPC Notify Scalability
Need only two modules
  xdc.useModule('ti.sdo.ipc.Notify'); xdc.useModule('ti.sdo.utils.MultiProc');
Configure notify to use mailbox driver
  /* configure the notify driver */ var NotifySetup = xdc.useModule('ti.sdo.ipc.family.vayu.NotifySetup'); NotifySetup.connections.$add( new NotifySetup.Connection({ driver: NotifySetup.Driver_MAILBOX, procName: "EVE1" }) );
Attach has no handshake
  /* setup IPC-notify with eve processor */ Notify_attach(Module.eveProcId, 0);

## Slide 21: Waiting on Two Input Sources
The DSP is blocked, waiting on input from two sources.
  Source 1: Waiting on the message queue for a new message.
  Source 2: Waiting on the semaphore for a post event.
How is this possible?
We use a SYS/BIOS Event instance. The event object has a binding to both the message queue and the semaphore.

## Slide 22: SYS/BIOS Event Object
DSP1
serverQ: MessageQ
Server
: Semaphore
1
: Event
: Sync
: Semaphore
2
3
4
5

## Slide 23: SYS/BIOS Event Object
DSP1
serverQ: MessageQ
Server
: Event
: Sync
: Semaphore
NotifyCB

## Slide 24: Create Phase
Create event object
  Event_Params_init(&eventP); event = Event_create(&eventP, NULL);
Create the message queue with sync and semaphore objects
  Semaphore_Params_init(&semP); semP.event = event; semP.eventId = Event_Id_01; /* message queue */ semP.mode = Semaphore_Mode_BINARY; sem = Semaphore_create(0, &semP, NULL); SyncSem_Params_init(&syncSemP); syncSemP.sem = sem; sync = SyncSem_create(&syncSemP, NULL); MessageQ_Params_init(&msgQueP); msgQueP.synchronizer = (Void *)sync; messageQ = MessageQ_create("ServerQue", &msgQueP);

## Slide 25: Execute Phase
Notify callback will post the event object directly.
  Event_post(event, Event_Id_00);
Server task will pend on event object.
  mask = Event_Id_01 | Event_Id_00; evts = Event_pend(event, Event_Id_NONE, mask, BIOS_WAIT_FOREVER); if (evts & Event_Id_00) { /* get payload from the notify queue */ job = Server_dequeueEvent(&Module.notifyQ); } if (evts & Event_Id_01) { /* get message from message queue */ MessageQ_get(Module.messageQ, (MessageQ_Msg *)&msg, BIOS_NO_WAIT); }

## Slide 26: Congratulations! End of Lab 3